## Slide 1: ACOMA
Latchesar Ionkov
Bradley Settlemyer
Dominic Manno
Adaptive Codec for Organic Molecular Archives
LA-UR-20-21586

## Slide 2: Goals
Provide high bit density
Adapt to oligos of different lengths
Adapt to different errors
  Error types
  Error rates for different types
  Spatial distribution of errors
  Missing whole oligos

## Slide 3: DNA Codec Challenges
Short sequences (at the moment)
Need for oligo identification
“Structural” oligo restrictions
  Homopolymer length
  CG Content
Sources of errors
  Synthesis
  Amplification
  Sequencing
Types of errors
  Substitutions
  Deletions
  Insertions

## Slide 4: Bit Packing
How to encode as many bits as possible per nucleotide (nt)?
Deal with “structural” errors only
Theoretical maximum: 2 b/nt
Existing methods:
  Goldman et al.: 1.58 b/nt
  Grass et al.: 1.78 b/nt
  Erlich et al.: 1.98 b/nt

## Slide 5: Bit Packing
Oligo counting
  Order oligos
  Reject the ones that fail criteria
AAAAA X
AAAAT 0
AAAAC 1
…
AAGGC 61
AAGGG XX
ATAAA 62
…
GGCGG 980
GGGAA XXX
…
GGGGG XXX
Total: 981 values (1.8 b/nt)

## Slide 6: ACOMA Codec
Level 0: bit packing
  How to convert between bits and nts
Level 1: single oligo layout
  Oligo identification (+ metadata error correction)
  Data
Level 2: error correction with multiple oligos
  Error correction for data

## Slide 7: ACOMA Bit Packing (Level 0)
Same as oligo counting
Homopolymer restrictions (H4G2):
  Maximum 4 for A, T, and C
  Maximum 2 for G
High CG content: handled at a higher codec level
It takes exponentially longer time to encode/decode
Limit up to 17 nts (32 bits data + 1 parity bit)
  Minimum 10,315,700,031 values (> 233)
  Data density: 33/17 = 1.94 b/nt
Oligo construction:
  Allows adding up to 17 nts fragments at the end
  Preserves the homopolymer length restrictions

## Slide 8: ACOMA Oligo Layout (Level 1)
Data
  N 33 bit blocks (32 bit + parity)
Metadata
  High CG flag (1 bit)
  Erasure Oligo flag for Level 2 (1 bit)
  Address/ID
Distributed metadata
  Split into N-1 blocks and place between the data blocks
  Additional block(s) with Reed-Solomon erasure at the end
  Used to discover deletions/insertions and align data blocks
Notes: - Need to correct for data shifting due to insertions and deletions
- Need to correct metadata errors within the oligo

## Slide 9: ACOMA Oligo Layout (Level 1)

## Slide 10: Block Alignment
Work in progress
Try to detect insertions and deletions by shifting the metadata blocks
Shift by 1 left/right and try to match the erasure code
Needs more analysis on how well it can align blocks and correct the metadata

## Slide 11: ACOMA Erasure Coding (Level 2)
2D erasure encoding
Group M oligos together
Encode erasure codes for data blocks from different oligos
Columns consist of blocks from different positions (to correct for spatial bias of errors)
Reed-Solomon erasure coding
Parity bit in data blocks used to detect errors

## Slide 12: ACOMA Examples

## Slide 13: ACOMA Parameters for 107 nt oligos
5 data blocks, 17 nts each = 85 nts: 1.94 b/nt
3*4 nts metadata blocks + 2*5 nts RS blocks = 22 nts
Metadata
  4 nts -> 186 values
  1863 = 6,434,856 values
  2 bits for High-CG and Erasure-Oligo flags
  1608714 addresses/IDs left (30.7 MB)
Level 1: 1.50 b/nt
Erasure Coding
  2 (1) Erasure Oligos for every 4 data oligos
  4*5*32 bits = 640 data bits per group for 606 (505) nts
Level 2: 0.996 (1.196) b/nt

## Slide 14: ACOMA Parameters for 110 nt oligos
5 data blocks, 17 nts each = 85 nts: 1.94 b/nt
3*5 nts metadata blocks + 2*5 nts RS block = 25 nts
Metadata
  5 nts -> 733 values
  7333 = 393,832,837 values
  2 bits for High-CG and Erasure-Oligo flags
  98,458,209 addresses/IDs left (1.8 GB)
Level 1: 1.45 b/nt
Erasure Coding
  2 (1) Erasure Oligos for every 4 data oligos
  4*5*32 bits = 640 data bits per group for 630 (525) nts
  Level 2: 0.969 (1.163) b/nt

## Slide 15: ACOMA Parameters for 204 nt oligos
10 data blocks, 17 nts each = 170 nts: 1.94 b/nt
8*3 nts metadata blocks + 2*5 nts RS blocks = 34 nts
Metadata
  3 nts -> 47 values
  478 = 23,811,286,661,761 values
  2 bits for High-CG and Erasure-Oligo flags
  5,952,821,665,440 addresses/IDs left (216 TB)
Level 1: 1.57 b/nt
Erasure Coding
  2 (1) Erasure Oligos for every 4 data oligos
  4*10*32 bits = 1280 data bits per group for 1182 (985) nts
  Level 2: 1.045 (1.254) b/nt

## Slide 16: Conclusions
Adaptive data packing
  Can use any oligo acceptance criteria, as long is it has reasonable locality
  Demonstrated good data density with homopolymer restrictions
Works with different oligo lengths
Detects deletions and insertions and can align data and metadata blocks
2D erasure coding that corrects for spatial error bias and allows multiple erasure oligos
Notes: Need more analysis on how well the metadata alignment works

## Slide 17: Extra

## Slide 18: Implementation: Fast Bit Packing/Unpacking
Oligo counting is not fast (and exponentially slower)
  It takes 85 µs on average to encode 13 bit value
  It takes 2 minutes on average to encode 33 bit value
Solution: lookup tables
  For each 4 nts prefix (256 values) generate a table that has the encoding for the first 20 bits of the value (1,048,576 32-bit values, 4 MB)
  Total space used 1 GB
  Algorithm:
    Pick table based on the previous 4 nts
    Lookup in the table the starting oligo using the first 20 bits
    Count for the last 13 bits
  It takes about 1 hour to generate tables, save to disk

## Slide 19: Rosetta Stone
Very long-term storage needs a way to bootstrap
Oligo(s) that define the ACOMA parameters:
  Number data blocks per oligo
  Length of data block (nt)
  Length of metadata blocks (nt)
  Number data oligos per erasure group
  Number of erasure oligos per erasure group
  Oligo admission/rejection criteria for bit packing!
    Function that receives an oligo and returns true/false
    Wasm or Knuth’s (M)MIX?
  Encoded with known ACOMA parameters
  Would be great if it all fits into one oligo

## Slide 20: Notes
Extra data in data block (can we use it for something?)
  Actual data density is 1.96 b/nt, not 1.94 b/nt (log2(10315700031) = 33.26)
  Depending on the 4 nts before the data block, there are some extra values that are lost per data block
  There is at least an extra bit available for each 4 data blocks
  Although the minimum number of values in 17 nts is 10,315,700,031 the average number is 13,388,713,708. Can we opportunistically use the extra values, if available?
Minimum metadata block length
  3 nts probably the shortest reasonable length
  For longer oligos (> 200 nt), instead of making the metadata blocks too small, it may make more sense to add more RS blocks
  Example: For the 197 nt oligo example, if we have 7 metadata blocks and 2 RS blocks, we’ll be able to address 4.6 TB of data.

## Slide 21: Implementation: High CG bit
Problem
  H4G2 encoding is asymmetric, we can’t just use the complementary if high CG
Solution
  Encode twice and use the one that has low CG
  Is it possible that both are high CG?